## Slide 1
Stormwater BMPs for Industries
“A Holistic Approach to LA River Revitalization Program”
Students: Wanxin Cai, Pooja Sinha, Luyue Zhang, Atosa Vahdati,
Honghong Li, Wenyu Li, Yudu Guo, Qiao Zhou, Xiaoshuang Zheng,and Xueyao Zhang
Supervisor: Professor Massoud (Mike) Pirbazari
August 2019
ENE510 - Water Quality Management and Practice

## Slide 2
https://cee.usc.edu/research/water-quality-research-group/swan/

## Slide 4
To the Visitors:
Your comments and suggestions are appreciated. Please direct your thoughts to Wanxin Cai at wxcai@alumni.usc.edu.
Thank you.

## Slide 5
Many industrial sites are exposed to rain and snow conditions. In particular, stormwater discharge, if not managed properly, can cause a variety of unwanted challenges for industrial sectors ranging from construction to manufacturing process to oil and gas to agriculture.
The industrial contaminants in stormwater discharges are largely dependent on:
The sector of industrial activity and type of activities occurring at the facility
Site-specific factors, such as topography, site outline, and soil
Contaminant type, based on the specific materials handled
Loading/unloading operations, outdoor storage, waste practice, and outside process activities
Illicit connection and non-stormwater discharges
Overview

## Slide 6
According to EPA, “the best way to prevent stormwater pollution from industrial sites is to minimize the use of materials and products in industrial activities that contaminate water and to minimize opportunities for stormwater to come into contact with industrial activities and polluting materials”.
Overview (cont’d)

## Slide 7
Table of Contents
    1. Background: LA River Revitalization
      Impact to LA River
      Relation to LA River Revitalization
    2. Stormwater BMPs
    3. Examples of Different Industries
    Summary and Discussion
    Future Work
    References

## Slide 8
Part 1
Background: LA River Revitalization

## Slide 9
Impact to LA River
Stormwater runoff includes all flows discharged into stormwater conveyance systems and receiving waters and includes both dry weather non-stormwater sources and wet weather stormwater runoff.
With the increasing urbanization of Los Angeles, the water quality in LA River has declined significantly. It is mostly due to untreated stormwater runoff from 2200 storm drain outlets. Storm drains carry runoff from streets, urban centers, industrial sites, and open spaces into streams, creeks, and rivers.
Industrial operations are major contributors of stormwater contamination in LA River. They are known to be sources of heavy metals, oily wastes, and a host of other contaminants. For example, manufacturing, shipping, storage operations, and other industrial activities that are exposed to stormwater can be sources of pollutants in stormwater.

## Slide 10
https://www.waterboards.ca.gov/rwqcb4/water_issues/programs/regional_program/Water_Quality_and_Watersheds/los_angeles_river_watershed/la_summary.shtml
Of the 1,319 dischargers enrolled under the general industrial storm water permit in the LA River Watershed, the largest numbers occur in the cities of Los Angeles (many within the community of Sun Valley), Vernon, South Gate, Long Beach, Compton, and Commerce.
Wholesale trade-durable goods, fabricated metal products, trucking & warehousing, and chemicals & allied products are a large component of these businesses based on their Standard Industrial Classification (SIC) codes.
This watershed has about twice the number of industrial stormwater dischargers as does the San Gabriel River Watershed and the most in the region. The locations of facilities with discharges covered by the general industrial stormwater permit are shown in the figure.
Impact to LA River (cont’d)
Locations of industrial stormwater discharges in the Los Angeles River Watershed

## Slide 11
Enhance Flood Storage
Enhance Water Quality
Enable Safe Public Access
Restore a Functional Riparian Ecosystem
Relation to LA River Revitalization
Four goals of LA River Revitalization

## Slide 12
Different plants can have very different stormwater quantities, flow patterns, and potential pollutants. Even different facilities of the same general industry may need different approaches to prevent stormwater pollution due to the different sizes or distances to LA River. Thus, it is essential to identify appropriate industrial stormwater Best Management Practices (BMPs) for these facilities to protect LA River water quality.
Stormwater BMPs provide economical and environmental-friendly incentives for achieving LA River revitalization.
Relation to LA River Revitalization (cont’d)
https://www.ioes.ucla.edu/project/how-competing-los-angeles-river-revitalization-plans-will-affect-surrounding-communities/

## Slide 13
    Background: LA River Revitalization
    Stormwater BMPs
      Common pollutants of concern in industrial stormwater
      California regulatory requirements
      Non-structural BMPs
      Advanced BMPs and structural control
    Examples of Different Industries
    Summary and Discussion
    Future Work
    References
Table of Contents

## Slide 14
Part 2
Stormwater BMPs

## Slide 15
California regulatory requirements
Common pollutants of concern in industrial stormwater
Potential pollutants associated with common industrial activities
Source: Stormwater Best Management Practice Handbook: Industrial and Commercial, California Stormwater Quality Association (CASQA), September 2014
Most common pollutants in industrial stormwater:
Total Suspended Solids (TSS)
Biological Oxygen Demand (BOD)
Chemical Oxygen Demand (COD)
Nutrients
Metals
Petroleum-derived hydrocarbons
Chlorides/salt
Temperature
Turbidity
pH

## Slide 16
In California, owners or operators of specific industrial facilities are required to obtain NPDES permit coverage by submitting Permit Registration Documents (PRDs) to be covered under the State Water Resources Control Board (SWRCB) Order No. 2014-0057-DWQ, National Pollutant Discharge Elimination System General Permit No. CAS000001, General Permit for Storm Water Discharges Associated with Industrial Activities (General Permit - SWRCB, 2014).
California regulatory requirements
General Permit for Storm Water Discharges Associated with Industrial Activities
The following parts of federal regulations contain Effluent Limitation Guidelines(ELGs) approved by USEPA for specific categories of industrial storm water discharges:
Cement Manufacturing
Fertilizer Manufacturing
Petroleum Refining
Phosphate Manufacturing
Steam Electric Power Generating
Wetting of Logs at Wet Deck Storage Areas
Coal Mining
Mineral Mining and Processing
Ore Mining and Dressing
Paving and Roofing Materials (tars and asphalt)
Landfills
Airport Deicing

## Slide 17
Facilities covered by National Pollutant Discharge Elimination System (NPDES) General Permit Storm Water Discharges Associated With Industrial Activities (General Permit) are required to prepare a Stormwater Pollution Prevention Plan (SWPPP). These include:
Facilities Subject to Storm Water Effluent Limitations Guidelines, New Source Performance Standards (NSPS), or Toxic Pollutant Effluent Standards Found in 40 Code of Federal Regulations, Chapter I, Subchapter N(Subchapter N)
Manufacturing Facilities
Oil and Gas/Mining Facilities
Hazardous Waste Treatment, Storage, or Disposal Facilities
Landfills, Land Application Sites, and Open Dumps
Recycling Facilities
Steam Electric Power Generating Facilities
Transportation Facilities
Sewage or Wastewater Treatment Works
California regulatory requirements
General Permit for Storm Water Discharges Associated with Industrial Activities (cont’d)

## Slide 18
The General Permit requires the dischargers to comply with the following:
Eliminate unauthorized non-stormwater discharges.
Develop and implement a facility specific stormwater pollution prevention plan (SWPPP), including a Monitoring Implementation Plan (MIP).
Implement minimum BMPs and advanced BMPs, if needed, and evaluate effectiveness (to the extent feasible).
Conduct monitoring, including visual observations and analytical monitoring of stormwater.
Compare analytical monitoring results to numeric action levels (NALs).
Perform Exceedance Response Actions (ERAs) when NALs are exceeded.
Certify and submit all compliance documents in the Storm Water Multi Application Reporting and Tracking System (SMARTS).
California regulatory requirements
General Permit for Storm Water Discharges Associated with Industrial Activities (cont’d)

## Slide 19
The owners and operators of industrial and commercial facilities must understand the relationship between the agencies, their jurisdictions, and the requirements of each, as shown in the figure below.
California regulatory requirements
General Permit for Storm Water Discharges Associated with Industrial Activities (cont’d)
Source: Stormwater Best Management Practice Handbook: Industrial and Commercial, California Stormwater Quality Association (CASQA), September 2014

## Slide 20
California regulatory requirements
Stormwater Pollution Prevention Plan (SWPPP)
Dischargers are required to prepare a SWPPP which includes:
Facility name and contact information
Site map
List of industrial materials
Description of potential pollution sources
Assessment of potential pollutant sources
Identified stormwater BMPs
Annual evaluation
Date that SWPPP was initially prepared and the date of each SWPPP amendment, if applicable

## Slide 21
Stormwater BMPs
Stormwater BMPs are measures to prevent or mitigate stormwater pollution, commonly categorized whether they are non-structural or structural. The General Permit categorizes BMPs as either minimum BMPs or advanced BMPs, which will be discussed in the following slides.
Structural BMPs: Design-based facilities that prevent the pollutants from reaching stormwater and treat or remove pollutants in stormwater.
Non-Structural BMPs: Generally consist of processes, prohibitions, procedures, schedule of activities, etc., that prevent pollutants associated with industrial activities from entering stormwater. They are generally economical and use low technology.
Minimum BMPs: All General Industrial Permit holders are required to conduct minimum BMPs.
Advanced BMPs: Will be required if a site has pollutant exceedances and cannot meet the discharge requirements. Selected according to activities and pollutants.
Note: Most minimum BMPs are non-structural, while some are structural.

## Slide 22
Minimum BMPs
Good housekeeping:
  Observe and maintain industrial activity outdoor areas
  Minimize or prevent material tracking
  Minimize dust generated
  Cleanup areas affected by rinse and wash water
  Cover stored industrial materials that can be readily mobilized by contact with stormwater
  Contain stored non-solid industrial materials or wastes
  Prevent disposal of rinse/wash waters
  Minimize flows of offsite stormwater and NSWDs into material handling areas
Source: Best Management Practices For Industrial Storm Water Pollution Control, Sacramento Stormwater Management Program
The following minimum BMPs are required by the General Permit and should be tailored to certain industrial activities or facilities.

## Slide 23
Preventative maintenance:
  Identify equipment and systems that may leak
  Observe the equipment and systems to detect leaks
  Establish procedures for equipment operation, maintenance, and repair
Spill and leak prevention and response
  Establish procedures and/or controls to minimize spills and leaks
  Develop and implement spill and leak response procedures to prevent industrial materials from being discharge
  Clean up spills and leaks promptly
  Identify and describe needed spill and leak response equipment
Source: Best Management Practices For Industrial Storm Water Pollution Control, Sacramento Stormwater Management Program
Minimum BMPs (cont’d)

## Slide 24
Material handling and waste management:
  Minimize handling of industrial materials or wastes that can be readily mobilized by contact with stormwater
  Contain non-solid industrial materials or wastes that can be transported or dispersed by the wind or contact with stormwater
  Cover industrial waste disposal and industrial material storage containers
  Divert run-on and stormwater away from stockpiled materials
  Clean spills that occur during handling
  Observe and clean outdoor material/waste handling equipment or containers
Source: Best Management Practices For Industrial Storm Water Pollution Control, Sacramento Stormwater Management Program
Minimum BMPs (cont’d)

## Slide 25
Erosion and sediment controls:
  Implement effective wind erosion controls
  Provide effective stabilization for inactive areas, finished slopes, and other areas prior to a forecasted storm event
  Maintain effective perimeter controls and stabilize site entrances
  Divert runoff and stormwater generated from within the facility away from erodible materials
  Properly design sediment basins
Employee training program
  Train stormwater team members
  Prepare or acquire training manuals
  Identify which personnel need to be trained
  Maintain training documentation
https://stormwater.pca.state.mn.us/index.php/Sediment_control_practices_-_Perimeter_controls_for_disturbed_areas
Minimum BMPs (cont’d)

## Slide 26
Quality assurance record keeping:
  Develop and implement management procedures to ensure implementation of plans
  Develop a method of tracking and recording program implementation
  Maintain implementation records (i.e., BMP deployment records, employee training logs, spill occurrence and clean-up records)
Source: Best Management Practices For Industrial Storm Water Pollution Control, Sacramento Stormwater Management Program
Minimum BMPs (cont’d)

## Slide 27
Advanced BMPs and structural control
1. Coolant/Oil recovery
Activities: metal removal discharges metal fines in the form of swarf, grindings, chips etc.
Typical problems: the coolants, metal fines, and tramp oil leak out of the outside container or are spilled in the process of loading onto a transport vehicle.
Typical pollutants: heavy metals (chromium, copper, manganese, lead, zinc), bacteria, fungi, chemicals in the coolant (corrosion inhibitors, emulsifiers, biocides), tramp oil, and decreased pH
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013
BMP:
Locate scrap bin on a concrete pad that drains into a containment sump

## Slide 28
Advanced BMPs and structural control
1. Coolant/oil recovery (cont’d)
b. Modify the scrap hopper for coolant/oil separation from the swarf while the coolant/oil is warm and less viscous
c. Use bins with built-in filtering screen to separate the scrap from the liquid chamber
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013

## Slide 29
Activities: metal cutting with gas burners, and welding metal with stick, wire or gas welders
Typical problem: fume exhausted outside comes in contact with rain and pollutes stormwater
Typical pollutants: oily air emissions, metal particles, gaseous metal, and vaporized flux
Advanced BMPs and structural control
2. Weld fume control
BMP: centralized cartridge filtration systems (figure on the left) and portable High-Efficiency Particulate Air (HEPA) filtration systems (figure on the right) are a couple of control methods in use today which phases out electrostatic precipitator systems. Air extraction units with mist or charcoal filters can also be used.
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013

## Slide 30
Activities: oil and other fluid dispensing and outside storage
Typical Problems: uncontained, expansions and contractions causes damage to container generating leaks. Dispensing oil, antifreeze, and other hazardous liquids may result in spills and leaks around the dispensing area. The leaked liquid can contact with stormwater or seep into soil and groundwater.
Typical Pollutants: oil, hydraulic fluid, antifreeze, paint, solvent, cleaners, petroleum hydrocarbons, toluene, ethylene glycol, etc.
Advanced BMPs and structural control
3. Drum and container containment
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013

## Slide 31
BMPs:
Potable metal storage building with built-in containment
Advanced BMPs and structural control
3. Drum and container containment (cont’d)
Use cone shaped drum covers to keep water off the top of the drums
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013

## Slide 32
c. Use containment palettes made by plastic or steel
d. Use double-walled storage tanks
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013
Advanced BMPs and structural control
3. Drum and container containment (cont’d)

## Slide 33
Typical problems: runoff from building with corrugated galvanized sheet metal roofs, siding, gutter, and downspout
Typical pollutants: zinc and iron
BMPs:
Avoid using galvanized sheeting
Clean and paint the exposed galvanized sheet
Contain and collect any liquids used in cleaning for proper disposal
Conduct regular inspections and maintenance
Collect and treat roof runoff
Advanced BMPs and structural control
4. Metal roof and siding coating treatment
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013

## Slide 34
Activities: cleaning parts and equipment with petroleum based cleaners
Typical problem: increase the risk of spilling and leakage getting spent cleaner into stormwater
Typical pollutant: petroleum hydrocarbons
Biological Parts Washer
Advanced BMPs and structural control
5. Biological based parts cleaner
BMPs:
Large Parts and frames cleaned in shot blast machine
Smaller parts should be cleaned in water based solution solution (caustic or other) or biological solution. The sludge from these washers are not hazardous.
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013

## Slide 35
Activities: pressure washing or steam cleaning of equipment, outdoor surfaces and/or vehicles
Typical problems: when equipment, pavement, vehicles, or buildings are washed outside, contaminants in the wash-water and the overspray mix with the stormwater runoff.
Typical pollutants: degreasers, organics, heavy metals, oil and grease, and pollutants from soaps
Advanced BMPs and structural control
6. Vehicle, pavement and building washing
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013

## Slide 36
BMPs:
Locate washing area on a well constructed, impervious surfaces with drains to other stormwater BMPs or storage tank.
Discharge the stormwater to a properly sized grassy swale or constructed wetland.
Discharge the washwater and stormwater to a collection sump for later disposal.
Discharge the stormwater through an oil/water separator.
Provide a package recirculation/treatment system for washing.
Contract with a mobile washer to wash the vehicles and ensure that they capture and remove the liquid and solids and properly dispose of them.
Perform the washing activities offsite at a commercial vehicle wash facility.
Advanced BMPs and structural control
6. Vehicle, pavement and building washing (cont’d)

## Slide 37
Activities: the outdoor storage of batteries and the long time storage of vehicles or battery-powered equipment outside
Typical problems: lead sulfate usually present in batteries can contaminate stormwater and soil.
Typical pollutants: soluble metals such as lead, nickel, or cadmium, sulfuric acid
Advanced BMPs and structural control
7. Battery storage
BMPs:
Batteries should be stored in contained area.
Use containment pallet to prevent any acid spillage and put it inside to keep stormwater away from contacting it.
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013

## Slide 38
Activities: wrecked or damaged vehicle storage or scrap metal recycling
Typical problems: fluids may leak due to the damage incurred and/or the damage may expose oily components of the vehicle. This can pollute stormwater, soil, and groundwater.
Typical pollutants: antifreeze (ethylene glycol), gasoline, oil, grease, brake fluid, diesel
Advanced BMPs and structural control
8. Wrecked vehicle storage and scrap metal recycling
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013

## Slide 39
Advanced BMPs and structural control
8. Wrecked vehicle storage and scrap metal recycling (cont’d)
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013
BMPs:
Ensure that all fluids are completely drained from the wrecked vehicles.
Provide impervious surface containments, drainage should pass through oil/water separators before being discharged.
Provide a roof to prevent stormwater contact with wrecked vehicles if possible.

## Slide 40
Activities: stripping coatings from metal and wood surfaces outdoors
Typical problems: stripping of wood and metal parts usually uses hazardous chemicals. High pressure water blasting produces increased runoff. Sand blasting creates lots of solids to dispose.
Typical pollutants: hazardous stripping chemicals, lead from old lead based paints, zinc chromate
Advanced BMPs and structural control
9. Paint stripping
BMP:
Use dry ice or baking soda abrasion type removal of old surface coatings
Use a removable ground cover before blasting to ease the cleaning efforts
Consider temporary or portable structure to contain and isolate the work and debris
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013

## Slide 41
Advanced BMPs and structural control
10. Brake Shoe Replacement
Activities: vehicle repair/brake shoe replacement
Typical problems: dust in the brake shoe/wheel housing is typically disturbed and can be released to outdoors when brake shoes are replaced.
Typical pollutants: asbestos, copper, total suspended solids
BMPs:
Use the Low Pressure/Wet Cleaning Method for dust removal
  Low Pressure/Wet Cleaning Method: This specially designed low-pressure spray equipment wets down the brake assembly and catches the runoff in a special basin to prevent airborne brake dust from spreading in the work area.
Use HEPA Vacuum System Method that can retain the micron sized particles
  HEPA Vacuum System Method: This type of enclosure and vacuum system has a special box with clear plastic walls or windows, which fits tightly around a brake or clutch assembly to prevent asbestos exposure.
https://instrumentnation.com/air-systems-av-55-electric-55-gallon-drum-lid-hepa-vacuum-system/
HEPA Vacuum System

## Slide 42
Advanced BMPs and structural control
11. Ozone generators for cooling towers
Activities: the use of cooling towers with the associated water treatment chemicals and blowdown discharges.
Typical problems: chemicals such as biocides, algaecides, and corrosion inhibitors are added to cooling towers to prevent biological growth and to reduce scaling and corrosion. Periodically cooling tower water must be blown down in order to remove sediment and particulate buildup in the cooling tower sump. This water can contain elevated levels of copper, zinc, and chemicals with high BOD5 and COD.
Typical pollutants: biocides, algaecides, fungicides, BOD, COD, suspended solids, metals (zinc and copper).
BMP: use ozone or UV light instead of chemicals to control biological growth and scaling. It is to be noted that a properly operated and controlled ozone treatment system will not allow microorganisms that secrete the glue-like substance to survive. Ozone will dissipate quickly and not be found in the blow down water. This reduces the overall chemical load found in the discharged water, making it easier to comply with regulations.

## Slide 43
Advanced BMPs and structural control
11. Ozone generators for cooling towers (cont’d)
Advantages
Safe and easy in use
Very effective in removing biofilms
Low maintenance costs
Ozone is produced on site and requires no additional disinfectants
Use ozone can reduce the need for blow down
Process for ozone treatment of cooling tower water
Most cooling tower ozone treatment systems include an air dryer, air compressor, water and oil coalescing filters, particle filter, ozone injectors, an ozone generator, and a monitoring/control system.
Ambient air is compressed, dried, and then ionized in the generator to produce ozone. Ozone is typically applied to cooling water through a side stream of the circulating tower water as is illustrated in the figure.
https://www.spartanwatertreatment.com/articles/Ozone-Treatment-for-Cooling-Towers-Federal-Technology-Alert.pdf

## Slide 44
Install a grassy filter strip and ensure that the storm water passes through the strip in sheet flow. Vegetated filter strips are best used on sites with sheet runoff.
Target Pollutants: sediment (TSS), PAH, metals, BOD, phosphorus, and oil & grease
Advanced BMPs and structural control
12. Grassy Filter Strip and Planter
Source: Industrial Stormwater Best Management Practices Manual, Oregon Department of Environmental Quality, February 2013
Best for smaller drainage basins with sheet flows
Cannot be used to convey large storms or concentrated flow discharge
Properly sized and maintained vegetated filter strips can have a removal efficiency of up to 80 percent for suspended solids
The graph on the right depicts the different simulated rainfall events of a specific intensity for durations from 30 to 180 minutes. (The slope of the vegetation cover is 10%)

## Slide 45
Constructed wetland uses natural processes involving wetland vegetation uptake, microbiological degradation, retention and settling.
Target pollutants: sediment (TSS), PAH, metals, BOD, phosphorus, and oil & grease
Advanced BMPs and structural control
13. Constructed wetland
Advantages
Disadvantages
Removes stormwater pollutants
Reduces peak flow
Provides wildlife habitat
Retains stormwater
Landscaping purpose
Must have a continuous base flow to maintain aquatic plants
Plants cannot endure drought or be submerged for a long time.
Cannot be placed on steep, unstable slopes
Public safety concerns
May have mosquito and vector breeding issues

## Slide 46
Advanced BMPs and structural control
13. Constructed wetland (cont’d)
https://stormwater.pca.state.mn.us/index.php/Types_of_stormwater_wetlands
There are five basic types of constructed wetland: shallow marsh, basin/wetland (formerly pond/wetland), extended detention (ED) wetland, pocket wetland, and gravel wetland.

## Slide 47
Advanced BMPs and structural control
13. Constructed wetland (cont’d)
https://stormwater.wef.org/2012/07/subsurface-gravel-wetlands-for-stormwater-management/
Concept schematic for subsurface gravel wetland

## Slide 48
Contaminant | Remove efficiency*
Heavy metals | 40 - 80%
Total Phosphorus | 40 - 80%
Total Nitrogen | 40 - 60%
Soluble reactive phosphorus | 75%
Nitrate | 65%
Total copper, lead, and zinc | 80 - 95%
TSS | 70%
Advanced BMPs and structural control
13. Constructed wetland (cont’d)
* Higher efficiencies are associated with use of O/G trap, larger pond/marsh area and volume.
Source: Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013
http://prj.geosyntec.com/npsmanual/constructedstormwaterwetlands.aspx
Different zones for constructed wetland

## Slide 49
Pervious pavement is a specially designed system that allows water to infiltrate through pavement and prevent it from becoming runoff. Used in uncontaminated areas where chemical or fine particle spill not likely occur.
Target pollutants: sediment (TSS), PAH, metals, BOD, phosphorus, and oil & grease
Advanced BMPs and structural control
14. Pervious pavement
Small amounts of petroleum contamination will be treated in the shallow soils or fillings beneath the porous material.
The porous pavement can drain larger pavement area if it is designed and installed properly.
Pervious pavement reduces stormwater runoff volume and peak flows.
https://www.1800sweeper.com/sweeping-services/permeable-pavement-cleaning

## Slide 50
Advanced BMPs and structural control
15. Oil/water (W/O) separators
There are two common types of oil/water separator: API (American Petroleum Institute) W/O separator and coalescing plate separator (CPS).
Activities: any site that has steel, equipment or vehicles stored outside and has a potential for oily or sediment-laden stormwater discharges.
Target pollutants: oil & grease and suspended solids
API oil/water separators are typically large-capacity, underground cement vaults designed with baffles to trap sediments and retain floating oils.
https://en.wikipedia.org/wiki/API_oil%E2%80%93water_separator

## Slide 51
Advanced BMPs and structural control
15. Oil/water (W/O) separators (cont’d)
Coalescing plate separator (CPS) has a smaller capacity and employs a series of oil-attracting plates.
http://www.elliswastewater.com/products/oil-water-separator/
Limitations of O/W separators
It cannot handle concentrated amounts of oily products and sediment in stormwater.
Antifreeze, degreasers, and detergents will break up oil into small droplets so it will allow the oil to pass through the separator.
It is not designed to treat heavy metal-bearing wastewater.
Coalescing plate separator (CPS)

## Slide 52
Advanced BMPs and structural control
16. Cartridge Filtration
Activity: operations with exposed copper and/or galvanized piping, galvanized siding and/or roofing materials, cathodic protection coatings of copper, or other exposed copper, brass, and/or zinc coated materials that are exposed to stormwater may have significant levels of these metals present in stormwater discharge. Operations involving heavy vehicle traffic may also have metals in their stormwater discharge such as copper from brake shoes and clutches or zinc from tire wear.
Target Pollutants: copper, zinc, PAH, total suspended solids
Vault type filter
Source: Industrial Stormwater Best Management Practices Manual, Oregon Department of Environmental Quality, February 2013

## Slide 53
Heavy Metals: 65 to 95%
Oil & Grease: up to 85% for a properly designed and sized system
Advanced BMPs and structural control
17. Cartridge Filtration (cont’d)
The installation of properly sized compost filtration units can remove significant amounts of both chemical and particulate forms of heavy metals like copper and zinc and reduce TSS levels in the storm water discharge. Colloidal particulate levels from clay soils should also be reduced effectively.
Removal efficiency
Source: Industrial Stormwater Best Management Practices Manual, Oregon Department of Environmental Quality, February 2013
Catch basin type filter

## Slide 54
A rain garden is a vegetated shallow depression that is designed to receive, retain, and infiltrate stormwater runoff from downspouts, piped inlets, or sheet flow from adjoining paved areas.
It can be applied in areas that are known as hot-spots (gas stations, transfer sites, and transportation depots). But impervious liner between in-situ soils and the planting soil medium is needed to reduce or eliminate the possibility of groundwater contamination
Target pollutants: sediment (TSS), metals, BOD, nutrients, and bacteria
Provides a level of treatment strictly through filtration processes that occur when the runoff moves through the soil material to the underdrain discharge point
Reduces stormwater runoff
Eliminates pollutant discharge
Advanced BMPs and structural control
18. Rain garden
http://www.jkdirtworks.com/html/rain_gardens.html
Notes: Rain garden is one of the most common stormwater BMPs.
It can reduce runoff, recharge groundwater, eliminate pollutant, provide habitat for wildlife, however, it requires maintenance, should be constructed on relatively flat site, and may result in vector breeding.
This is the general removal efficiency of common contaminants for all kinds of rain garden. Some removal efficiency vary in a big range, cuz it depends largely on media in the structure.

## Slide 55
    Background: LA River Revitalization
    Stormwater BMPs
    Examples of Different Industries
      Scrap metal recycling
      Metal fabrication/finishing industry
      Food industry
      Petroleum industry
    Summary and Discussion
    Future Work
    References
Table of Contents

## Slide 56
Part 3
Examples of Different Industries

## Slide 57
Each scrap recycling facility is unique in regards to sources, type, and volume of contaminated stormwater discharges. As a result, there is variation in pollutants for which BMPs may be necessary to address. The table below indicates the common pollutants and its source associated with activities.
I. Scrap metal recycling
Source: Industrial Stormwater Fact Sheet Series, U.S. EPA Office of Water, Dec 2006

## Slide 58
I. Scrap metal recycling (cont’d)
A combination of appropriate BMPs will yield the most effective stormwater management for minimizing the offsite discharge of pollutants via stormwater runoff.
Example
Treat stormwater from 40 acre recycling yard in Schnitzer Steel, Portland, OR.
Pollutants: aluminum, cadmium, chromium, copper, iron, lead, nickel, zinc and total suspended solids (TSS)
A multi-stage 600gpm WaveIonics treatment system (see next slide) consisting of electrocoagulation, clarification, filtration and carbon polishing are used to treat stormwater.
The effective BMPs include:
Regular cleanup, collection and containment of debris in storage areas
Housekeeping practices
Spill control
Employee training
Oil/water separators
Wet ponds
Proprietary filter devices
Other BMPs based on activities

## Slide 59
Uses electrocoagulation enhanced filtration technology
Removes total suspended solids, heavy metals, emulsified oil, bacteria, sulfides, oil & grease, silica, phosphorus, BOD, COD, PCB, PAHs.
Suitable for applications such as oil & gas produced water, mine process water, industrial storm and wastewater, and construction stormwater
Modifications can be applied to the process based on effluent objectives
http://www.watertectonics.com/technology/waveionics/
Video demonstration: http://www.watertectonics.com/technology/waveionics/
http://www.watertectonics.com/technology/waveionics/
WaveIonics technology
I. Scrap metal recycling (cont’d)

## Slide 60
II. Metal fabrication/finishing industry
Pollutants conveyed in stormwater discharges from facilities involved with metal fabrication/finishing will vary. The activities, pollutant sources, and pollutants detailed in the following table are commonly found at metal fabricating/finishing facilities.
Source: Industrial Stormwater Fact Sheet Series, U.S. EPA Office of Water, Dec 2006

## Slide 61
II. Metal fabrication/finishing industry (cont’d)
A variety of BMP options may be applicable to eliminate or minimize the presence of pollutants in stormwater discharges from metal fabrication/finishing facilities. Since most of the operations occur indoors, minimizing exposure of pollutants to stormwater runoff is very important. The effective BMPs include:
Regular cleanup, collection and containment of debris in storage areas
Housekeeping practices
Spill control
Employee training
Use of covers, indoor storage, and indoor operations
Grass swales
Sedimentation ponds
Other suitable BMPs according to activities

## Slide 62
II. Metal fabrication/finishing industry (cont’d)
Silver Bullet — A technology for metal fabrication/finishing facilities
The Sivler Bullet is an automatic stormwater treatment system. It can treat stormwater at the rate of up to 200 gallon per minute with high removal efficiency.
Target pollutants:
Metals (Aluminum, Copper, Iron, Lead, Magnesium, Zinc)
Oil & grease
Total suspended solid
COD
BOD
Enterococcus
Fecal Coliform
Other applicable industries:
Scrap metal recyclers
Municipal waste collection facilities
Secondary metal refiners
Manufacturing facilities
Sand blasting companies
Plating and galvanizing facilities
Municipal waste sorting facilities
Truck maintenance facilities
https://brashind.com/

## Slide 63
Silver Bullet treatment process
https://brashind.com/
https://brashind.com/
Stormwater is pretreated to remove large particles and pollutants
Followed by flocculation to form large particles, then settled out by gravity settling
Remaining suspended particles (100 micron to 5 micron) are removed by filter
Dissolved pollutants are removed by an ion bed
Disinfected by UV radiation
II. Metal fabrication/finishing industry (cont’d)

## Slide 64
III. Food industry
The food industries have requirements for sanitary conditions, so that raw materials through final product be protected from stormwater.
Therefore, the contamination of stormwater from these activities are primarily from the loading and unloading of products and raw materials; spillage and leaks from tanks and containers stored outdoors; waste management practices; pest control; and improper connections to the storm sewer.
The activities, pollutant sources, and pollutants detailed in table are commonly found at food products facilities.
Source: Industrial Stormwater Fact Sheet Series, U.S. EPA Office of Water, Dec 2006

## Slide 65
III. Food industry(cont’d)
Maintain, pump, and use grease traps and interceptors to prevent overflows. Keep grease bins covered and contained. Recycle grease and oil. Reduce the amount of grease washed down the drain by scraping off trays, grills, and pans into a grease can. Do not pour grease and oil into sinks, floor drains, parking lots or streets.
For small spills or drips, put absorbent material like kitty litter on the spill to contain it. Sweep up the used absorbent, place in a secure bag, and deposit in a secure trash bin.
Keep garbage dumpster lids closed to keep rain and rodents out. Keep litter from accumulating around docks by providing trash receptacles and encouraging employees to use them. Never dispose of liquids in the dumpster. Inspect for leaks on a regular basis and have bins replaced when necessary.
Dispose of grease and oil safely
Maintain garbage dumpsters
Clean spills
https://www.countyofnapa.org/DocumentCenter/View/2904/BMPs-for-Food-Service-Facilities---Brochure-PDF
Non-structural BMPs

## Slide 66
Parking
Milk Storage Tanks
Storage Building
Pavement
III. Food industry (cont’d)
Example: Double Scoop ice cream company
Effective BMPs
Minimum BMPs (discussed in Part 2)
Oil/water separator
Rain garden
Vegetated Swales
Cartridge filtration
Permeable pavement
Constructed wetland
Other suitable BMPs according to activities
Double Scoop ice cream company
Pre-BMP site map
Source: Stormwater Management for Industrial Activities, U.S. EPA Office of Water, Dec 2006

## Slide 67
Parking
Milk Storage Tanks
Storage Building
Pavement
Tree well
Permeable pavement
Green roof
Rain Gardens
vegetated swale
Cisterns
Double Scoop ice cream company
Pre-BMP site map
Source: Stormwater Management for Industrial Activities, U.S. EPA Office of Water, Dec 2006
Infiltrate stormwater into ground
Detain roof stormwater runoff
Detain stormwater runoff and remove pollutants
Collect excess roof stormwater runoff
Detain stormwater runoff and remove pollutants
Detain stormwater runoff and remove pollutants
III. Food industry (cont’d)
Example: Double Scoop ice cream company

## Slide 68
IV. Petroleum industry
Major pollutants in petroleum industry
Total suspended solids (TSS)
Total dissolved solids(TDS)
Oil and grease
Chemical oxygen demand (COD)
Chlorides
Barium
Naphthalene
Benzene
Lead
Arsenic
Fluoride
Petroleum-derived hydrocarbons
Effective BMPs
Minimum BMPs (discussed in Part 2)
Drum & container containment
Tank containment
Biological based parts cleaners
Oil/water separator
Other suitable BMPs according to activities
Pollutants in stormwater runoff from facilities involved with the exploration and production techniques will vary depending on the type and characteristics of formations, pollutants present, and waste management controls.

## Slide 69
Oil/Water Separators
Biological Based Parts Cleaners
Constructed Wetlands
Drum & Container Containment
Tank Containment
IV. Petroleum industry (cont’d)
Remove petroleum hydrocarbons
Detain stormwater and remove pollutants
Prevent damages and leakages
Prevent damages and leakages
Remove oil and sediment
https://www.schneider-electric.com/en/work/solutions/for-business/oil-and-gas/

## Slide 70
    Background: LA River Revitalization
    Stormwater BMPs
    Examples of Different Industries
    Summary and Discussion
    Future Work
    References
Table of Contents

## Slide 71
Part 4
Summary and Discussion

## Slide 72
Summary and Discussion
Relation to LA River revitalization:
Stormwater BMPs provide economical and environmental-friendly incentives for achieving LA River revitalization, protecting LA River from being polluted by industrial stormwater discharges.
Regulations to protect LA River:
Owners or operators of specific industrial facilities are required to obtain General Permit and prepare Stormwater Pollution Prevention Plan to protect beneficial uses of water resources.
Stormwater BMPs for industries:
Minimum BMPs should be implemented by all General Industrial Permit holders.
Advanced BMPs can be chosen and tailored based on industrial activities to ensure the compliance with regulations.
The following industries are presented as examples:
Scrap metal recycling
Metal fabrication/finishing industry
Food industry
Petroleum industry

## Slide 73
With the increasing urbanization of Los Angeles, the water quality in LA River has declined significantly. Stormwater BMPs will play a more and more important role in achieving LA River Revitalization.
The stormwater BMPs discussed in this study should be identified and tailored according to the industry type, facility sizes, industry activities, and other factors.
Some industrial activities can be applied to a variety of other industrial facilities, and the selected BMPs can be tailored to the specific industrial activity or operation.
It would be more effective to implement a combination of different BMPs to address stormwater runoff at the facility.
Summary and Discussion (cont’d)

## Slide 74
    Background: LA River Revitalization
    Stormwater BMPs
    Examples of Different Industries
    Summary and Discussion
    Future Work
    References
Table of Contents

## Slide 75
Part 5
Future Work

## Slide 76
Future Work
(This section is in progress)
The use of BMPs in several European countries is currently being reconsidered to address efficiency, practicality, and cost-effectiveness. Other countries such as China are also adopting new programs and technologies to better manage and treat stormwater.
This section briefly discusses stormwater case studies in several countries.

## Slide 77
  Case study I:
  Coal-powered electricity generating facilities in China
Pollutants may be present in stormwater as a result of outdoor activities such as: material handling and transport operations, waste disposal, and deposition of airborne particulate matter.
The primary and largest potential source is ash refuse piles. Pollutants such as vanadium, sodium, sulfur, and nickel are all common elements found in oil ash. Silica, alumina, ferric oxide, calcium oxide, magnesium oxide, and sodium and potassium oxides are all common.
The activities, pollutant sources, and type of pollutants detailed in the following table are commonly found at steam electric generating facilities, including coal handling areas.
Source: Industrial Stormwater Fact Sheet Series, U.S. EPA Office of Water, Dec 2006

## Slide 78
Example: Stormwater management in coal handling area, China
Treatment steps:
Collect stormwater
Intercept and temporarily store trash
Discharge early-period stormwater due to its heavy load pollutants
Filtration
Temporarily store stormwater
Coagulation, clarification, deep filtration, and disinfection
Reuse for recreation, toilet flushing, and landscape irrigation
  Case study I:
  Coal-powered electricity generating facilities in China (cont’d)

## Slide 79
Example: Stormwater management in coal handling area, China
https://www.hlhbzj.com/id557787.html
Recreation
Toilet flushing
Landscape irrigation
Stormwater collection
Screen
Pretreatment
Filtration
Storage tank
Pump
Integrated treatment device
Reuse
  Case study I:
  Coal-powered electricity generating facilities in China (cont’d)

## Slide 80
    Background: LA River Revitalization
    Stormwater BMPs
    Examples of Different Industries
    Summary and Discussion
    Future Work
    References
Table of Contents

## Slide 81
Part 6
References

## Slide 82
References
  Stormwater Best Management Practice Handbook: Industrial and Commercial, California Stormwater Quality Association (CASQA), September 2014.
  Best Management Practices For Industrial Storm Water Pollution Control, Sacramento Stormwater Management Program, June 1992.
  Industrial Stormwater Best Management Practices Manual, by Dennis Jurries and Krista Ratliff, February 2013.
  https://www.waterboards.ca.gov/rwqcb4/water_issues/programs/regional_program/Water_Quality_and_Watersheds/los_angeles_river_watershed/la_summary.shtml
  https://www.ioes.ucla.edu/project/how-competing-los-angeles-river-revitalization-plans-will-affect-surrounding-communities/
  https://instrumentnation.com/air-systems-av-55-electric-55-gallon-drum-lid-hepa-vacuum-system/
  https://www.spartanwatertreatment.com/articles/Ozone-Treatment-for-Cooling-Towers-Federal-Technology-Alert.pdf
  https://stormwater.pca.state.mn.us/index.php/Types_of_stormwater_wetlands
  https://stormwater.wef.org/2012/07/subsurface-gravel-wetlands-for-stormwater-management/
  http://prj.geosyntec.com/npsmanual/constructedstormwaterwetlands.aspx

## Slide 83
References
  https://www.1800sweeper.com/sweeping-services/permeable-pavement-cleaning
  https://en.wikipedia.org/wiki/API_oil%E2%80%93water_separator
  http://www.elliswastewater.com/products/oil-water-separator/
  http://www.jkdirtworks.com/html/rain_gardens.html
  Industrial Stormwater Fact Sheet Series, U.S. EPA Office of Water, Dec 2006
  http://www.watertectonics.com/technology/waveionics/
  https://brashind.com/
  https://www.countyofnapa.org/DocumentCenter/View/2904/BMPs-for-Food-Service-Facilities---Brochure-PDF
  Stormwater Management for Industrial Activities, Section I, U.S. EPA Office of Water, Dec 2006.
  Stormwater Management for Industrial Activities, Section N, U.S. EPA Office of Water, Dec 2006.
  Stormwater Management for Industrial Activities, Section O, U.S. EPA Office of Water, Dec 2006.
  Stormwater Management for Industrial Activities, Section U, U.S. EPA Office of Water, Dec 2006.

## Slide 84
References
  Stormwater Management for Industrial Activities, Section AA, U.S. EPA Office of Water, Dec 2006.
  https://www.schneider-electric.com/en/work/solutions/for-business/oil-and-gas/
  https://www.hlhbzj.com/id557787.html
  Los Angeles River Revitalization Master Plan, City of Los Angeles Department of public Works Bureau of Engineering, April 2007.
  Green Infrastructure for Los Angeles: Addressing Urban Runoff and Water Supply Through Low Impact Development, City of Los Angeles, April 17, 2009.
  Water Quality Compliance Master Plan for Urban Runoff: Clean Stormwater/Urban Runoff Master Plan, Watershed Protection Division Bureau of Sanitation Department of Public Works, City of Los Angeles, May 2009.
  https://www.epa.gov/npdes/stormwater-discharges-industrial-activities
  https://www.waterboards.ca.gov/water_issues/programs/stormwater/docs/industrial/2014indgenpermit/atta.pdf
  State Water Resources Control Board (SWRCB) Order No. 2014-0057-DWQ, National Pollutant Discharge Elimination System General Permit No. CAS000001, General Permit for Storm Water Discharges Associated with Industrial Activities.

## Slide 85
References
  Industrial Stormwater Best management practices Guidebook, Minnesota pollution control agency, Version 1.1, April 2015.
  Stormwater Best Management Practice Handbook: New Development and Redevelopement, California Stormwater Quality Association (CASQA), January 2003.
  https://www.waterboards.ca.gov/water_issues/programs/stormwater/igp_20140057dwq.shtml
  https://www.waterboards.ca.gov/rwqcb4/water_issues/programs/stormwater/municipal/watershed_management/los_angeles/upper_reach2/15-01-27LARUR2WMARevWMP.pdf
  https://escholarship.org/content/qt42m433ps/qt42m433ps.pdf
  https://www.waterboards.ca.gov/rwqcb2/water_issues/programs/stormwater/muni/nrdc/16%20bmp_refguide%5B1%5D.pdf
  http://www.waterresources.saccounty.net/stormwater/documents/industrial-BMP-manual.pdf
  http://sccd.org/wp-content/uploads/2015/07/Infiltration-Trenches.pdf
  https://www.epa.gov/sites/production/files/2015-11/documents/swppp_guide_industrial_2015.pdf
  https://www.epa.gov/sites/production/files/2015-07/documents/tmdl-sw_permits11172008.pdf
  https://www.waterboards.ca.gov/rwqcb4/water_issues/programs/regional_program/Water_Quality_and_Watersheds/los_angeles_river_watershed/la_summary.shtml

## Slide 86
References
  https://www.waterboards.ca.gov/water_issues/programs/stormwater/igp_20140057dwq.shtml
  https://www.pca.state.mn.us/sites/default/files/wq-strm3-26.pdf
  https://www.epa.gov/sites/production/files/2015-10/documents/sector_f_primarymetals.pdf
  https://stormwaterx.com/stormwaterx_products/aquip/
  https://www.deq.state.or.us/wq/wqpermit/docs/indbmp021413.pdf